## Slide 1: Enzyme Linked Immunosorbent Assay (ELISA)

## Slide 2: ELISA
Enzyme Linked Immunosorbent Assay (ELISA)
Term Was Coined By Engvall and Pearlmann in 1971
Different Types
  Sandwich
  Indirect
  Competitive
Similar To RIA, Except No Radiolabel
Can Be Used To Detect Both Antibody and Antigen
Very Sensitive, pg/mL
Relies on Monoclonal Abs

## Slide 4: Sandwich ELISA
2 Antibodies Required
Must Recognize Different Epitopes
1st Antibody Is Referred To As Capture Ab
2nd Antibody Detection Ab
2nd Antibody Is Biotinylated
Enzymes Commonly Used: HRP (Horse Radish Peroxidase) And AKP (Alkaline Phosphatase)
Substrate is TMB (Chromogen)

## Slide 5: ELISA Plate
96 well plate
Made of plastic on which protein can be adsorbed (bind) easily
Usually done overnight @ 4C
Special buffer used that will not denature Ab and maximize binding
Blocking step ensures no empty spaces are left
Blocking reagent is often 10% FBS

## Slide 6: Standard Curve
Serial dilutions of the cytokine being measured
Exact concentration is needed
A plot of concentration (pg/mL or ng/mL) is plotted against OD (optical density)

## Slide 7: Sensitivity Of Elisa
Typically the lowest cytokine concentration that can be detected above negative control
2-3 S.D Above Mean Background Signal
Depending On Antibody Pair Used Sensitivity Varies
Ex. 10 pg/mL

## Slide 8: General Protocol
Dilute capture Ab @ 1-4 g/mL In Binding Solution
Ex. Stock Solution Of Capture Ab: 0.5 mg/mL And Capture Ab Recommended Conc. 2 g/mL
First Question To Ask Yourself ?
  How much volume would I use?
  Count 16 wells for S.C+
  3 wells for Negative Controls
  Your Samples (usually in triplicates)
  Add them up and multiply by 100 L (typical volume used per well)
Let’s Say 4 mL Needed
  You will need 16 L of capture Ab
Add capture Antibody, Seal plate (minimize evaporation)
Incubate overnight at 4C

## Slide 9: Binding Solution
Pharmingen Recommended Reagent
0.1 M Na HPO4, adjust to pH 9.0 or to pH 6.0 with 0.1 M NaH2PO4
pH Is Very Important, If Wrong No Binding
Some Antibodies Require pH 6.0
  Ex. Antibodies for mIL-10, mMCP-1, mTNF, rGM-CSF).

## Slide 10: Blocking
Blocking Reagent 10% FBS in PBS
Alternatively 1% BSA (Immunoassay Grade)
Filter To Remove Particulates
Plate Is Brought To R.T
Add 200 L per well Blocking Buffer
Wait For 2 Hours At R.T
Why Do We Block?

## Slide 11: After Blocking
Wash x3 With PBS/Tween (detergent)
Add Standards + Samples
Samples Are Typically Supernatants From Cultures Or Patient Serum/Plasma
Use 100 L
Often Dilution Is Required If Signal Is Too Strong
Standards?

## Slide 12: Standard Preparation
Standards Are Diluted in Blocking Buffer/Tween
Start By Labeling eight, 1 mL Eppendorf Tubes
Prepare Highest Conc. Tube (1 mL)
Fill The Remaining Tubes with 0.5 mL Blocking Buffer
Serially Dilute From Top To Lowest

## Slide 13
Assume You Have A Stock Tube @ 2ng/L, Volume 5 L
Usually Remaining Standard Cytokine Is Thrown Away
Thawing-Unthawing Affects Cytokine

## Slide 14: After Standard Preparation
Add Samples, Standards, Negative Control
  Negative Control Should Be The Buffer You Use Dilute Standard or Culture Medium
Incubate For 2 Hrs at R.T
Aspirate And Wash 5x

## Slide 16: Addition Of Detection Ab
Avidin is a Hen Oviduct Protein
Avidin has very high affinity for biotin (B vitamin)
B vitamin is conjugated on the detection Ab
Add Working Detector @ 100 L/well
  Ex. Stock Detection Antibody=0.5mg/mL
  You need to prepare 5 mL @ 1  g/mL
  Use 10  L of Stock Antibody
  Add 5 L of Enzyme (Avidin-HRP)
  Dilution is 1:1000
Incubate for 60 mins @ R.T
Wash 6x

## Slide 17: Addition Substrate
Prepare Substrate by Mixing 1:1 volume
Add 100 L/well
Incubate for 10 mins, Avoid Formation of Excessively Bright Color (Spec will not be able to read)
Terminate Reaction by Adding 0.5 M H2SO4 (color changes from blue to yellow)

## Slide 18: Read Plate At Appropriate Wavelength (=450 nm)

## Slide 19: Data Analysis

## Slide 20: Graph Plotting