## Slide 1
Lecture: Forensic Serology - Immunoassays
Antibody/Antigen reaction provides the means of generating a measurable result.
“Immuno” refers to an immune response that causes the body to generate antibodies.
“Assay” refers to a test.
An immunoassay is a test that uses immunocomplexing when antibodies and antigens are brought together.

## Slide 2: Immunoassay Definitions
An antibody is a protein produced in the body to a foreign substance.
An antigen is the substance that the body is trying to eliminate by mounting an immune response.
An analyte is anything measured by a laboratory test.
Immunoassays may measure either the antigen or antibody.
Immunoassays use one or more select antibodies to detect analytes of interest.
Analyte may be naturally present.
Analyte may be those that the body produces.
Analyte may be those that does not normally occur in the body.
Notes: Antibodies are produced as part of the body’s immune response to protect itself. For instance a immunoassay may test for the presence of antibodies to cancer molecules. If the antibodies are present, the invading cancer cells are also present.

## Slide 3: Structure of Antibodies
Antibodies are a type of protein called immunoglobins.
Most common protein is immunoglobin G.
Notes: FAB region: contains the antigen (Ag) binding site that varies between different antibodies.
Fc region has a constant structure within an antibody class.

## Slide 4: Preparation of Polyclonal Antibodies
Polyclonal antiserum is generated in animals (sheep, rabbits or goats) with the introduction of antigens into the animals bloodstream.
The antiserum (serum from blood containing the desired antibodies) contains a mixture of antibodies, each of which may bind to different antigen binding sites (epitopes).
Antiserum contains a mixture of antibodies.
This mixture of antibodies are called ployclonal antibodies.
An antigen that has multiple sites for antibody binding is called a mutivalent antigen.
Notes: The process of making an antiserum begins with the injection of an antigen of interest into an animal. The antigen may also be called an immunogen because it can stimulate an immune response. Over time, the animal’s immune system produces antibodies to the injected antigen. Blood is collected from the animal and the serum is isolated from the blood. This serum is usually rich in antibodies that recognize the antigen and is called the antiserm.

## Slide 5: Preparation of Monoclonal Antibodies
Monoclonal antibodies are highly specific for a single epitope on a multivalent antigen.
They are produced from a single cell line using hybridoma technology and mouse myeloma cell lines.
Notes: Hybridomas are antibody producing tumor cells that may produce many copies of the same antibody and grow easily in lab cell culture.
An advantage of monoclonal antibodies is that the hybridoma cell line that produces them is potentially “imortal” and can produce the same antibodies consistently and indefinitely. A polyclonal antisera produced by immunization of animals can vary from animal to animal.

## Slide 6: Categories of Immunoassay Tests
Competitive
Noncompetitive
Homogeneous
Heterogeneous
Labels may be applied to either the antibody..
..or the antigen.
Notes: All immunoassays require the use of labeled material in order to measure the amount of antigen or antibody present. A label is a molecule that will react as part of the assay so that a change in signal can be measured in the blood:reagent solution. Examples of a label include a radioactive compound, n enzyme that causes a change in color in a solution, or a substance that produces light.

## Slide 7: Competitive Assays
In a competitive format, unlabeled analyte (usually the antigen) in the test sample is measured by its ability to compete with the labeled antigen in the immunoassay.
In a competitive immunoassay, less label measured in the assay means more of the unlabeled (test sample) antigen is present.
There are two versions of the competitive format:
  One step format
  Two step format
Notes: The unlabeled antigen blocks the ability of the labeled antigen to bind because the binding site on the antibody is already occupied. Thus, in a competitive immunoassay, less label measured in the assay means more of the unlabeled (test sample) antigen is present. The amount of antigen is the test sample is inversely related to the amount of label measured in the competitive format

## Slide 8: Noncompetitive Assays
Noncompetitive assay formats give the highest level of sensitivity and specificity.
They are normally used to measure critical analytes such as cardiac and hepatitis markers.
Noncompetitive assay formats can use either one step or two step methods.
In the two step assay format, there are wash steps in which the sandwich binding complex is isolated and washed to remove excess unbound labeled reagent.
In noncompetitive assays, the measurement of the labeled analyte (usually the antibody) is directly proportional to the amount of antigen present in the sample.
Notes: Noncompetitive assay format is referred to as a “sandwich” assay because the analyte is bound between two highly specific antibody reagents

## Slide 9: Heterogeneous and Homogeneous Immunoassays Methods
Immunoassays that require separation of the bound Ab-Ag* complex are referred to as being heterogeneous immunoassays.
Those that do not require separation are referred to as homogeneous immunoassays.
Homogeneous methods have generally been applied to the measurement of small analytes such as abused and therapeutic drugs.

## Slide 10: Radioimmunoassay (RIA)
Radioimmunoassay (RIA) techniques were developed in the 1960s and use radioactive isotopes as a label
Notes: The amount of radioactivity measured is indicative of the amount of analyte present.
The left test (noncompetitive sandwich format) the amount of label present directly correlates with the amount of antigen present.
In the competitive format, the amount of antigen is inversely correlated with the amount of label present.
RIA tests are still used today particularly for the detection of very low quantities of analytes.
Problems with handling and disposing of radioactive materials make RIA tests in the clinical and drug screening labs rare.

## Slide 11: Enzyme Immunoassay (EIA)
In enzyme immunoassays (EIA), enzyme labels are used instead of radioactive labels.
Typical enzyme labels include alkaline phosphatase, horseradish peroxidase and b-galatosidase.
EIA tests typically use a change in color, emmission of light or other signal.

## Slide 12: Enzyme Immunoassay (ELISA)
Enzyme Linked Immunosorbent Assay (ELISA) is an application of solid phase heterogeneous sandwich immunoassay that combines enzyme-antibody label reagent with a solid phase bound antibody.
Notes: Elisa is a type of EIA

## Slide 13: Fluorescence Polarization Immunoassay (FPIA)
Fluorescence Poloarization Immunoassy (FPIA) is a type of homogeneous competitive fluoresence immunoassay.
With competitive binding, antigen from the specimen and antigen-fluorescein (AgF) labeled reagent compete for binding sites on the antibody.
FPIA is used to provide accurate and sensitive measurements of small toxicological analytes such as therapeutic drugs and drugs of abuse.
The FPIA reagent includes the antibody reagent, a tracer, and a pretreatment detergent.

## Slide 14: Fluorescence Polarization Immunoassay
FPIA uses three concepts to measure specific analytes in a homogeneous format:
  Fluorescence
  Rotation of molecules in solution
  Polarized light

## Slide 15: Fluorescence
Fluorescein is a fluorescence label that absorbs light at 490 nm and releases this energy at 520 nm.
Larger molecules rotate more slowly in solution that smaller molecules.
Because of this, we can distinguish between the smaller antigen-fluorescein (AgF) label from antibody bound antigen-fluorescein (Ab-AgF).

## Slide 16: Polarized Light
When polarized light is absorbed by AgF, the molecule rotates quickly before the light is emitted as fluorescence.
When the larger-sized Ab-AgF complex absorbs the polarized light, it rotates more slowly and the light is emitted in the same plane and the detector can measure it.
FPIA results in an inverse response curve such that lower levels of patient analyte result in a higher signal.

## Slide 17: Accuracy and Precision
Accuracy means the assay is determining the correct concentration.
Precision is the reproducibility of an assay.
Sensitivity and specificity are subsets of accuracy and precision.
An assay that has the ability to produce accurate and precise results and does not produce false positives is considered specific.
An assay that has the ability to produce accurate and precise results and does not produce false negatives is said to be sensitive.
Notes: Accuracy is the ability to measure the correct concentration of the analyte in the sample.
Immunoassays may be both accurate and precise, accurate but not precise, precise but not accurate, or neither precise nor accurate.

## Slide 18: Calibrators and Controls
Calibrators are solutions with known concentration values that establish the relationship between the signal response prodused during the assay and the analyte concentration.
It is important that the user follow the manufacturer’s treatment criteria for the calibrators to ensure that the calibration is accurate.
The manufacturer also has to chose the correct matrix for the calibrators has a signal response that mimics the signal from patient samples

## Slide 19: Calibrators and Controls
Controls are samples that contain known concentrations of analyte and are used to monitor the accuracy and precision of the assay and analyzer.
If the control’s concentration is within 2 SDs of the QC average, then the assay is said to be in control and that the results collected are valid

## Slide 20: Assay Interferences
One step assays may be prone to interferences that affect both sensitivity and specificity.
In general sequential assays are more likely to yield accurate results by elimination the adverse contribution of binding proteins, endogenous interfering substances and general matrix effects due to the extra wash step.
Notes: Most often due to agents that interfer with the binding of antibodies to antigens for a variety of reasons.