## Slide 1: Radioimmunoassay (RIA)

## Slide 2: RIA
to determine the concentration of an antigen in solution
involves the separation of a protein (from a mixture) using the specificity of antibody - antigen binding and quantization using radioactivity
Competitive binding assay
Originally developed by Yalow and Berson in 1960 for measurement of insulin in plasma

## Slide 3: Principle
The amount of Ab per tube is kept constant, the amount of antigen added (known or unknown) is the variable parameter.
The added antigen will be distributed between a bound (B) and a free (F) fraction.
This distribution is governed by the association constant (KA) of the Ab:

## Slide 4
To measure this distribution B-F ,a small but constant amount of labeled antigen ("tracer") is added to the reaction. Eventually, there will be a competition reaction between this small but constant amount of "tracer" and the "cold" antigen for a limited amount of antibody.
Since B + F = Ag* = constant, measurement of either B OR F is sufficient.

## Slide 5
4Ag* + 4 Ab 4Ag*Ab
4Ag + 4Ag* + 4Ab 2Ag*Ab + 2AgAb + 2Ag* + 2 Ab
12Ag + 4Ag* + 4Ab Ag*Ab + 3AgAb + 3Ag* + 9Ag

## Slide 6: RIA
Reagents
  Tracer: labeled antigen
  Antibody
  Standards: Known concentrations of unlabeled antigen
  Unknown samples (unlabelled antigen= analyte)

## Slide 7: RIA- The Technique
A mixture is prepared of
  radioactive antigen
  antibodies against that antigen.
Known amounts of unlabeled ("cold") antigen are added to samples of the mixture. These compete for the binding sites of the antibodies.
At increasing concentrations of unlabeled antigen, an increasing amount of radioactive antigen is displaced from the antibody molecules.
The antibody-bound antigen is separated from the free antigen in the supernatant fluid, and the radioactivity of each is measured.
From these data, a standard binding curve, can be drawn.
The samples to be assayed (the unknowns) are run in parallel.
After determining the ratio of bound to free antigen in each unknown, the antigen concentrations can be read directly from the standard curve.

## Slide 8: Standard Curve & Unknown Sample

## Slide 9: Preparation of the Reagents:
Antibodies
Polyclonal antibodies are made by injecting an animal with the antigen, then purifying the antibody from serum.
  Molecules smaller than ~1000 d are not generally immunogenic
  Steroids are covalently bond to protein carriers which are immunogenic, antibodies can then be purified and their specificity verified.
  Monoclonal Antibodies

## Slide 10: Characteristics of Tracer
Must Have Similar Binding Properties as Unlabeled Ligand
Internally Labeled Ligand
  14C and 3H
Externally Labeled Ligand
  131I and 125I

## Slide 11
1. Internally labeled molecules
  Typically, tritium (3H) is the label, sometimes 14C.
  Usually purchased commercially.
  Used only for small molecules like steroids or drugs.
  Merit : the tracer immunologically behaves exactly as the cold hormone, thus theoretically perfect.
  Demerit : beta-radiation is weak and therefore more difficult to measure, thus practically cumbersome.
  Beta rays have low penetrating power: the radioactive sample needs to be mixed with a scintillator fluid (flour); the produced light is measured by use of a photomultiplier ("beta-counter").
Notes: Primary flour= 2,5-diphenyloxazole (POP), secondary flour= 1,5-bis (5-phenyloxazol-2-yl) benzene (POPOP)

## Slide 12
2. Externally labeled molecules
  Typically, 125I is the label.
  Merit: often produced in the research lab itself.
  gamma-radiation has high penetrating power, is therefore easy to measure, thus practical to use.
  Demerit : the tracer immunologically does not always behave exactly as the cold hormone, due to iodination damage
  shelf-life of iodinated protein is < 4 weeks.
  Usually, 125I will take the place of a hydrogen atom on on the ring of tyrosine.
  Sometimes, a radioactively labeled molecule needs to be conjugated to the protein.

## Slide 13: Preparation of the Reagents:
Iodination of the antigen
I125 is the radioactive label most often used.
  Gamma emission at 35keV
  Available commercially as NaI
Proteins with surface tyrosine groups can be oxidized with commercially available products.
I125 can be added to the tube and will bind to the oxidized residues
Column chromatography is used to purify the tracer

## Slide 14: RIA –Merits & Demerits
versatility : using the same principle, almost any biomolecule can be assayed
fast (usually 2 days or less)
sensitive (comparable to the most sensitive bioassays, that is < ng/ml)
large capacity : thousands of samples/day
specific (antibody-dependent)
use of radioactivity: hazardous
expensive equipment (gamma or beta counter)
Does require approval and training to work with radioactive materials
Modifying an assay procedure can be difficult and time consuming

## Slide 15: Separation of Bound and Free Ligand
  Antibody labeled tubes can be simply decanted
  Liquid-phase antibodies need to be precipitated
    Use a second antibody
    PEG
    Electrophoresis
    Gel Filtration
    Adsorption Chromatography
    Partition Chromatography
      Dialysis
    Fractional Precipitation
      Centrifugation
      Filtration

## Slide 16: Applications of Radioimmunoassays
Endocrinology
  Insulin, HCG, Vasopressin, T3, T4, TSH,
  Detects Endocrine Disorders
  Physiology of Endocrine Function
Pharmacology
  Morphine, digitoxin or digoxin ,
  Detect Drug Abuse or Drug Poisoning
  Study Drug Kinetics
Epidemiology
  Hepatitis B
Clinical Immunology
  Antibodies for Inhalant Allergens
  Allergy Diagnosis
  anti-DNA antibodies
Oncology
  Carcinoembryonic Antigen
  Early Cancer Detection and Diagnosis

## Slide 17
Gamma Counter
Scintillation Counter